## Slide 1
W4111 – Introduction to Databases Module II (1), NoSQL (1)
© Donald F. Ferguson, 2025

## Slide 2
Module II Kickoff
2 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 3: Course Modules – Reminder

## Slide 4
Module II – DBMS Architecture and Implementation
Overview and Reminder
4 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 5: Module II – DBMS Architecture and Implementation
Covered for the relational model.
Database Systems: The Complete Book (2nd Edition) by Hector Garcia-Molina (Author), Jeffrey D. Ullman (Author), Jennifer Widom (Author)

## Slide 6: Module II – DBMS Architecture and Implementation
Database Systems: The Complete Book (2nd Edition) by Hector Garcia-Molina (Author), Jeffrey D. Ullman (Author), Jennifer Widom (Author)

## Slide 7: Purpose of Database Systems
Data redundancy and inconsistency: data is stored in multiple file formats resulting induplication of information in different files
Difficulty in accessing data
  Need to write a new program to carry out each new task
Data isolation
  Multiple files and formats
Integrity problems
  Integrity constraints (e.g., account balance > 0) become “buried” in program code rather than being stated explicitly
  Hard to add new constraints or change existing ones
In the early days, database applications were built directly on top of file systems, which leads to:
Notes: 7

## Slide 8: Purpose of Database Systems (Cont.)
Atomicity of updates
  Failures may leave database in an inconsistent state with partial updates carried out
  Example: Transfer of funds from one account to another should either complete or not happen at all
Concurrent access by multiple users
  Concurrent access needed for performance
  Uncontrolled concurrent accesses can lead to inconsistencies
    Ex: Two people reading a balance (say 100) and updating it by withdrawing money (say 50 each) at the same time
Security problems
  Hard to provide user access to some, but not all, data
Database systems offer solutions to all the above problems
Notes: 8

## Slide 9: DBMS Arch.

## Slide 10
Data Management
Today
Storage
Load/save things quickly.
Database Systems: The Complete Book (2nd Edition) by Hector Garcia-Molina (Author), Jeffrey D. Ullman (Author), Jennifer Widom (Author)

## Slide 11
Disks/Storage Input/Output (IO)
11 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 12: Disks as Far as the Eye can See

## Slide 13: Classification of Physical Storage Media
Can differentiate storage into:
  volatile storage: loses contents when power is switched off
  non-volatile storage:
    Contents persist even when power is switched off.
    Includes secondary and tertiary storage, as well as batter-backed up main-memory.
Factors affecting choice of storage media include
  Speed with which data can be accessed
  Cost per unit of data
  Reliability

## Slide 14: Storage Hierarchy
CPU
From: Database System Concepts, 7th Ed.
CPU
Cache
RAM
RAM
RAM
Bus
Disk Cntler
Network Cntler
Network

## Slide 15
Slower
Cheaper
Unlimited
Faster
More expensive
Limited
Memory Hierarchy
From: Database System Concepts, 7th Ed.

## Slide 16
Memory Hierarchy (Very Old Numbers – Still Directionally Valid)
These numbers are ancient.
But, it does give an idea of
  Price
  Performance
The general observation is that
  Performance goes up 10X/level.
  Price goes up 10x per level.
Note: One major change is improved price performance of SDD relative to HDD for large data.

## Slide 17: Storage Hierarchy (Cont.)
primary storage: Fastest media but volatile (cache, main memory).
secondary storage: next level in hierarchy, non-volatile, moderately fast access time
  Also called on-line storage
  E.g., flash memory, magnetic disks
tertiary storage: lowest level in hierarchy, non-volatile, slow access time
  also called off-line storage and used for archival storage
  e.g., magnetic tape, optical storage
  Magnetic tape
    Sequential access, 1 to 12 TB capacity
    A few drives with many tapes
    Juke boxes with petabytes (1000’s of TB) of storage

## Slide 18
Hard Disk Drive
”Spinning mechanical drives are less and less common.”
Rapidly being replaced by solid state drives (SSDs).
The legacy of hard drives does influence the architecture of the software and I/O.

## Slide 19: Disk Configuration
Database Systems: The Complete Book (2nd Edition) by Hector Garcia-Molina (Author), Jeffrey D. Ullman (Author), Jennifer Widom (Author)
Components of disk I/O delay
  Seek: Move head to cylinder/track.
  Rotation: Wait for sector to get under head.
  Transfer: Move data from disk to memory.

## Slide 20
Hard
Disk
Drive
Solid
State
Drive
Hard Disk versus Solid State Disk

## Slide 21: Flash Storage
NOR flash vs NAND flash
NAND flash
  used widely for storage, cheaper than NOR flash
  requires page-at-a-time read (page: 512 bytes to 4 KB)
    20 to 100 microseconds for a page read
    Not much difference between sequential and random read
  Page can only be written once
    Must be erased to allow rewrite
Solid state disks
  Use standard block-oriented disk interfaces, but store data on multiple flash storage devices internally
  Transfer rate of up to 500 MB/sec using SATA, and up to 3 GB/sec using NVMe PCIe
STAT = Serial Advanced Technology Attachment NVMe = Non-Volatile Memory Express
PCIe = Peripheral Component Interconnect Express

## Slide 22: Logical Block Addressing
Concept:
  The unit of transfer from a “disk” to the computer’s memory is a “block. Blocks are usually relatively large, e.g. 16 KB, 32 KB, ... ...
  A program that reads or write a single byte, requires the database engine (or file system) to read/write the entire block.
The address of a block in the entire space of blocks is:
  (Device ID, Block ID)
  Block ID is simple 0, 1, 2, ... ...
The disk controller and disk implementation translate the logical block address into the physical address of blocks.
The physical address changes over time for various reasons, e.g. performance optimization, internal HW failure, write to new SSD location, etc.

## Slide 23: Logical/Physical Block Addressing
The mapping from LBA to physical block address can change over time.
Internal HW failure.
SSD writes in a funny way.
  You have to erase before writing.
  So, the SSD (for performance)
    Writes to an empty block.
    Erase the original block.
Performance optimization on HDD
  Based on block access patterns.
  Place blocks on cylinder/sector/head in a way to minimize:
    Seek
    Rotate
Processor
Buffer
Mech Controller

## Slide 24: I/O Architecture
How we normally think of disks and I/O.
Large scale environments
The bus-controller connection is over some kind of network.
The disk controller is at the disks, and basically a “computer” with SW.
Network is either
  Standard communication network, or
  Highly optimized I/O network.

## Slide 25: Magnetic Disks
Read-write head
Surface of platter divided into circular tracks
  Over 50K-100K tracks per platter on typical hard disks
Each track is divided into sectors.
  A sector is the smallest unit of data that can be read or written.
  Sector size typically 512 bytes
  Typical sectors per track: 500 to 1000 (on inner tracks) to 1000 to 2000 (on outer tracks)
To read/write a sector
  disk arm swings to position head on right track
  platter spins continually; data is read/written as sector passes under head
Head-disk assemblies
  multiple disk platters on a single spindle (1 to 5 usually)
  one head per platter, mounted on a common arm.
Cylinder i consists of ith track of all the platters
Notes: Mention: checksums, bad sector remapping

## Slide 26: Magnetic Disks (Cont.)
Disk controller – interfaces between the computer system and the disk drive hardware.
  accepts high-level commands to read or write a sector
  initiates actions such as moving the disk arm to the right track and actually reading or writing the data
  Computes and attaches checksums to each sector to verify that data is read back correctly
    If data is corrupted, with very high probability stored checksum won’t match recomputed checksum
  Ensures successful writing by reading back sector after writing it
  Performs remapping of bad sectors

## Slide 27: Performance Measures of Disks
Access time – the time it takes from when a read or write request is issued to when data transfer begins. Consists of:
  Seek time – time it takes to reposition the arm over the correct track.
    Average seek time is 1/2 the worst case seek time.
      Would be 1/3 if all tracks had the same number of sectors, and we ignore the time to start and stop arm movement
    4 to 10 milliseconds on typical disks
  Rotational latency – time it takes for the sector to be accessed to appear under the head.
    4 to 11 milliseconds on typical disks (5400 to 15000 r.p.m.)
    Average latency is 1/2 of the above latency.
  Overall latency is 5 to 20 msec depending on disk model
Data-transfer rate – the rate at which data can be retrieved from or stored to the disk.
  25 to 200 MB per second max rate, lower for inner tracks

## Slide 28: Performance Measures (Cont.)
Disk block is a logical unit for storage allocation and retrieval
  4 to 16 kilobytes typically
    Smaller blocks: more transfers from disk
    Larger blocks: more space wasted due to partially filled blocks
Sequential access pattern
  Successive requests are for successive disk blocks
  Disk seek required only for first block
Random access pattern
  Successive requests are for blocks that can be anywhere on disk
  Each access requires a seek
  Transfer rates are low since a lot of time is wasted in seeks
I/O operations per second (IOPS)
  Number of random block reads that a disk can support per second
  50 to 200 IOPS on current generation magnetic disks

## Slide 29: Performance Measures (Cont.)
Mean time to failure (MTTF) – the average time the disk is expected to run continuously without any failure.
  Typically 3 to 5 years
  Probability of failure of new disks is quite low, corresponding to a “theoretical MTTF” of 500,000 to 1,200,000 hours for a new disk
    E.g., an MTTF of 1,200,000 hours for a new disk means that given 1000 relatively new disks, on an average one will fail every 1200 hours
  MTTF decreases as disk ages

## Slide 30: Performance Measures of Disks
Access time – the time it takes from when a read or write request is issued to when data transfer begins. Consists of:
  Seek time – time it takes to reposition the arm over the correct track.
    Average seek time is 1/2 the worst case seek time.
      Would be 1/3 if all tracks had the same number of sectors, and we ignore the time to start and stop arm movement
    4 to 10 milliseconds on typical disks
  Rotational latency – time it takes for the sector to be accessed to appear under the head.
    4 to 11 milliseconds on typical disks (5400 to 15000 r.p.m.)
    Average latency is 1/2 of the above latency.
  Overall latency is 5 to 20 msec depending on disk model
Data-transfer rate – the rate at which data can be retrieved from or stored to the disk.
  25 to 200 MB per second max rate, lower for inner tracks
From: Database System Concepts, 7th Ed.

## Slide 31: Logical Block Addressing (https://gerardnico.com/wiki/data_storage/lba)
CHS addresses can be converted to LBA addresses using the following formula:
  LBA = (( C x HPC ) + H ) x SPT + S – 1
  where,
  C, H and S are the cylinder number, the head number, and the sector number
  LBA is the logical block address
  HPC is the number of heads per cylinder
  SPT is the number of sectors per track
  Devices have configuration and metadata APIs that allow storage manager to
    Map between LBA and CHS
    To optimize block placement
    Based on access patterns, statistics, data schema, etc.

## Slide 32
I/O Architecture
Redundant Array of Independent Disks (RAID)

## Slide 33: RAID (https://en.wikipedia.org/wiki/RAID)
“RAID (redundant array of independent disks) is a data storage virtualization technology that combines multiple physical disk drive components into a single logical unit for the purposes of data redundancy, performance improvement, or both. (…)
RAID 0 consists of striping, without mirroring or parity. (…)
RAID 1 consists of data mirroring, without parity or striping. (…)
RAID 2 consists of bit-level striping with dedicated Hamming-code parity. (…)
RAID 3 consists of byte-level striping with dedicated parity. (…)
RAID 4 consists of block-level striping with dedicated parity. (…)
RAID 5 consists of block-level striping with distributed parity. (…)
RAID 6 consists of block-level striping with double distributed parity. (…)
Nested RAID
  RAID 0+1: creates two stripes and mirrors them. (…)
  RAID 1+0: creates a striped set from a series of mirrored drives. (…)
  JBOD RAID N+N: With JBOD (just a bunch of disks), (…)”

## Slide 34: RAID-0 and RAID-1
Single “Fast” Disk
Single “Reliable” Disk
Two physical disks make one single, logical fast disk
Two physical disks make one single, logical reliable disk

## Slide 35: Mixed RAID Modes
Stripe
And
Mirror

## Slide 36: RAID-5
Improved performance through parallelism
  Rotation/seek
  Transfer
Availability uses parity blocks
  Suppose I have 4 different data blocks on the logical drive A: A1, A2, A3, A4.
  Parity function: Ap = P(A1,A2,A3,A4)
  Recovery function: A2=R(Ap,A1,A3,A4)
During normal operations:
  Read processing simply retrieves block.
  Write processing of A2 updates A2 and Ap
If an individual disk fails, the RAID
  Read
    Continues to function for reads on non-missing blocks.
    Implements read on missing block by recalculating value.
  Write
    Updates block and parity block for non-missing blocks.
    Computes missing block, and calculates parity based on old and new value.
  Over time
    “Hot Swap” the failed disk.
    Rebuild the missing data from values and parity.
A
B
C
D
E
One Big Logical Disk
Is actually 5 smaller “logical” disks.
Logical disk data spread over 5 physical disks.

## Slide 37: Very Simple Parity Example
Even-Odd Parity
  b[i] is an array of bits (0 or 1)
  P(b[i]) =
    0 is an even number of bits = 1. {P([0,1,1,0,1,1])= 0
    1 if an odd number of bits = 1. {P(0,0,1,0,1,1]= 1
  Given an array with one missing bit and the parity bit, I can re-compute the missing bit.
    Case 1: [0,?,1,0,1,1] has P=0. There must be an EVEN number of ones and ?=1.
    Case 2: [0,?,1,0,1,1] has P=1. There must be an ODD number of ones and ?=0.
Block Parity applies this to a set of blocks bitwise
  A1=[0,1,0,0,1,1]
  A2=[1,1,1,0,0,0]
  A3=[0,0,0,1,0,1]
  Pa=[1,0,1,1,1,0]
If I am missing a block and have the parity block, I can re-compute the missing block bitwise from remaining blocks and parity block.


## Slide 38
NoSQL
38 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 39
Concepts
39 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 40: Overview (I) (https://en.wikipedia.org/wiki/NoSQL)
A NoSQL (originally referring to "non SQL" or "non relational")[1] database provides a mechanism for storage and retrieval of data that is modeled in means other than the tabular relations used in relational databases. Such databases have existed since the late 1960s, but did not obtain the "NoSQL" moniker until a surge of popularity in the early twenty-first century,[2] triggered by the needs of Web 2.0 companies such as Facebook, Google, and Amazon.com.[3][4][5] NoSQL databases are increasingly used in big data and real-time web applications.[6] NoSQL systems are also sometimes called "Not only SQL" to emphasize that they may support SQL-like query languages.[7][8]
Motivations for this approach include: simplicity of design, simpler "horizontal" scaling to clusters of machines (which is a problem for relational databases),[2] and finer control over availability. The data structures used by NoSQL databases (e.g. key-value, wide column, graph, or document) are different from those used by default in relational databases, making some operations faster in NoSQL. The particular suitability of a given NoSQL database depends on the problem it must solve. Sometimes the data structures used by NoSQL databases are also viewed as "more flexible" than relational database tables.[9]

## Slide 41: Overview (I) (https://en.wikipedia.org/wiki/NoSQL)
Many NoSQL stores compromise consistency (in the sense of the CAP theorem) in favor of availability, partition tolerance, and speed. Barriers to the greater adoption of NoSQL stores include the use of low-level query languages (instead of SQL, for instance the lack of ability to perform ad-hoc joins across tables), lack of standardized interfaces, and huge previous investments in existing relational databases.[10] Most NoSQL stores lack true ACID transactions, … …
Instead, most NoSQL databases offer a concept of "eventual consistency" in which database changes are propagated to all nodes "eventually" (typically within milliseconds) so queries for data might not return updated data immediately or might result in reading data that is not accurate, a problem known as stale reads.[11] Additionally, some NoSQL systems may exhibit lost writes and other forms of data loss.[12] Fortunately, some NoSQL systems provide concepts such as write-ahead logging to avoid data loss.[13] For distributed transaction processing across multiple databases, data consistency is an even bigger challenge that is difficult for both NoSQL and relational databases. Even current relational databases "do not allow referential integrity constraints to span databases."[14]

## Slide 42: Simplistic Classification (https://medium.com/swlh/4-types-of-nosql-databases-d88ad21f7d3b)
We will see OLAP in a future lecture.
Relational is the foundational model.
We covered graphs and examples.
Subject of this lecture and part of HW3

## Slide 43: One Taxonomy

## Slide 44: Another Taxonomy

## Slide 45: Use Cases
Motivations
Massive write performance.
Fast key value look ups.
Flexible schema and data types.
No single point of failure.
Fast prototyping and development.
Out of the box scalability.
Easy maintenance.
What is wrong with SQL/Relational?
Nothing. One size fits all? Not really.
Impedance mismatch. – Object Relational Mapping doesn’t work quite well.
Rigid schema design.
Harder to scale.
Replication.
Joins across multiple nodes? Hard.
How does RDMS handle data growth? Hard.
Need for a DBA.
Many programmers are already familiar with it.
Transactions and ACID make development easy.
Lots of tools to use.

## Slide 46
Documents
46 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 47: Example Document – An Order
There are 5 entity types on the form:
  A “copy of” customer information.
  Links (via productCode) to products
  Order
  OrderDetails
  Comments
But OrderDetails and Comments are somehow different from the others.
  These are arrays of objects
  That are sort of “inside” the order.
These are weak entities, but relational does not always handle these well.

## Slide 48: Relational vs Document
The key difference?
Relational DB attributes are atomic.
Document DB attributes may be multi-valued. composite and lists.
Relational
Document

## Slide 49: UI Interface and Logical Data Model
{
customerName: “Columbia University”,
contact: {
name: “Lord Voldemort”,
phone: “+1 212-555-6666”
},
address: {
line1: “520 W 120th St.”
line2: “Floor 4”,
… …
}
orders: [
{
number: …,
… …
details: [
… …
]
}
]
}
Note to DFF: Start
~/Dropbox/000/000-A-Current-Examples/W4111-FastAPI-IMDB-Solution
~/Dropbox/000/000-A-Current-Examples/current-dashboard

## Slide 50
MongoDB
50 | W4111-2025S-08-Module-II-NoSql-1 © Donald F. Ferguson, 2025

## Slide 51: MongoDB Concepts
RDBMS | MongoDB | MongoDB
Database | Database | Database
Table | Collection | Collection
Tuple/Row | Document | Document
column | Field | Field
Table Join | Embedded Documents | Embedded Documents
Primary Key | Primary Key (Default key _id provided by MongoDB itself) | Primary Key (Default key _id provided by MongoDB itself)
Database Server, Client, Tools, Packages |  | 
mysqld/Oracle |  | mongod
mysql/sqlplus |  | mongo
DataGrip |  | Compass
pymysql |  | pymongo

## Slide 52: Core Operations
Basic Operations:
  Create database
  Create collection
  Create-Retrieve-Update-Delete (CRUD):
    Create: insert()
    Retrieve:
      find()
      find_one()
    Update: update()
    Delete: remove()
More Advanced Concepts:
  Limit
  Sort
  Aggregation Pipelines
    Merge
    Union
    Lookup
    Match
    Merge
    Sample
    ... ...
We will just cover the basics for now and may cover more things in HW or other lectures.

## Slide 53: find()
Note:
  MongoDB uses a more pymysql approach, e.g. an API, than pure declarative languages like SQL.
  The parameters for find() are where the declarative language appears.
The basic forms of find() and find_one() have two parameters:
  filter expression
  Project expression
You can use the Compass tool and screen captures for some HW and exam answers.
What if I want the answer in a Jupyter Notebook?

## Slide 54: Generate Code
Choose Export to Language.
Copy into the notebook.
The export has an option to include all the connection setup, choosing DB, ... ...
Switch to Notebook

## Slide 55: Result is not Quite You Expect
The query returns documents that match.
  The document is “Large” and has and episodes and seasons.
  If you do a $project requesting episodes/episode content,
    You get all episodes in the documents that match.
    Not just the episodes with the scene/location.
    Projecting array elements from arrays whose elements are arrays is complex and baffling.
You also get back something (a cursor) that is iterable.

## Slide 56: Result is not Quite You Expect
The query returns documents that match.
  The document is “Large” and has and episodes and seasons.
  If you do a $project requesting episodes/episode content,
    You get all episodes in the documents that match.
    Not just the episodes with the scene/location.
    Projecting array elements from arrays whose elements are arrays is complex and baffling.
You also get back something (a cursor) that is iterable.
Net for HWs and exams:
We will keep the queries simple.
The language is as complex as SQL, and we spent several weeks on the language.
Let’s take a look in the Jupyter Notebook on some create and insert functions.
But, first, the datamodel impedance mismatch concept.

## Slide 57: More Fun – Data Types
SQL
MongoDB
pymysql
Python
pymongo

## Slide 58: (Some) MongoDB CRUD Operations
Create:
  db.collection.insertOne()
  db.collection.insertMany()
Retrieve:
  db.collection.find()
  db.collection.findOne()
  db.collection.findOneAndUpdate()
  ... ..
Update:
  db.collection.updateOne()
  db.collection.updateMany()
  db.collection.replaceOne()
Delete:
  db.collection.deleteOne()
  db.collection.deleteMany()
pymongo maps the camel case to _, e.g.
  findOne()
  find_one()
There are good online tutorials:
https://www.tutorialspoint.com/python_data_access
https://www.tutorialspoint.com/mongodb/index.htm

## Slide 59: (Some) MongdoDB Pipeline Operators
https://www.slideshare.net/mongodb/s01-e04-analytics

## Slide 60: MongoDB Checkpoint
You can see that MongoDB has powerful, sophisticated
  Operators
  Expressions
  Pipelines
We have only skimmed the surface. There is a lot more:
  Indexes
  Replication, Sharding
  Embedded Map-Reduce support
  ... ...
We will explore a little more in subsequent lectures, homework, ... ...
You will have to install MongoDB and Compass for HW4 and final exam.